## Slide 1
Smart Home IoT
Room Temperature & Humidity Monitor
CAPSTONE 4 • AI-assisted project documentation
CAPSTONE 4 • 1/7

## Slide 2
Problem & Objectives
Room conditions can change unnoticed.
• Measure temperature and relative humidity
• Report readings as CSV over USB serial
• Alert with LEDs and buzzer when thresholds are crossed
CAPSTONE 4 • 2/7

## Slide 3
System Architecture
DHT22 sensor → ESP32 → Serial Monitor
↘ Green/Red LEDs
↘ Buzzer
Baseline is offline; Wi-Fi dashboard is future work.
CAPSTONE 4 • 3/7

## Slide 4
Bill of Materials
ESP32 DevKit V1 — ₹401.20 (observed listing)
DHT22 sensor — ₹212.40 (observed listing)
LEDs, resistors, buzzer, wiring, USB supply — estimates
Estimated subtotal: ₹926.60 before shipping; re-check prices.
CAPSTONE 4 • 4/7

## Slide 5
Firmware Logic
Sample every ~2.5 seconds
1. Read temperature and humidity
2. If read fails: print SENSOR_ERROR; red LED on
3. If temperature ≥ 30 °C OR RH ≥ 70%: ALERT
4. Otherwise: NORMAL
5. Print timestamp, values, and status
CAPSTONE 4 • 5/7

## Slide 6
Verification & Automation
Test plan includes normal, threshold, sensor-fault, boundary, and cadence cases.
BOM.csv → AUTOMATION.py → formatted BOM.xlsx
Important: tests are planned, not executed; add simulator/hardware evidence after running.
CAPSTONE 4 • 6/7

## Slide 7
Safety, Privacy & Next Steps
• Verify sensor pinout, pull-up, board pins, and buzzer current
• Use regulated USB power; transistor driver where needed
• No cloud or personal data in baseline
• Not a certified safety device; calibrate before real use
Future: authenticated Wi-Fi dashboard, logging, calibration
CAPSTONE 4 • 7/7